## Slide 1: Signals and Train Control Engineering
DLU Log Decoder
By: Mark Karlov

## Slide 2: Presentation Outline
Presentation Contents
  Objective / Problem Statement
  Project Goal
  Resources
  Understanding Raw DLU Logs
  Program Overview – Frontend
  Program Overview – Backend
  Design Challenges
  Demonstration
  Current Status
  Future Enhancements
  Questions

## Slide 3: Objective / Problem Statement
OMAP is needed to analyze raw DLU logs
OMAP has a terrible UX design for side-by-side parameter comparison
# of Parameters: 1800 - 3100
# of Pages: 30 - 53

## Slide 4: Objective / Problem Statement
OMAP offers a way to extract ALL data to a processed .txt file
This process is very SLOW, and sometimes inaccurate
# of Records:
3500 - 6000

## Slide 5: Project Goal
Create a GUI that allows users to
  Add, remove, upload files
  Search and select specific parameters to analyze
Create a Backend that
  Decodes raw DLU logs into processed .txt files
  Parses processed .txt files based on
    Parameter selection
    Change from previous record

## Slide 6: Benefit to TTC
This program allows users to
  Observe parameter change
  Observe selective parameters
This means that
  Engineers can analyze data faster
  Engineers can short-circuit to the problem source faster

## Slide 7: Resources
Richard Tam & Edward W. Chan
OMAP
ATO/ATP Base Files
Compressed DLU Logs
Vim
HTML, CSS, JS, C++, Bash

## Slide 8: Understanding Raw DLU Logs
Raw DLU Logs are decompressed DLU logs
Binary charset
Under UTF-8 encoding, each character represents a byte
UTF-8 Byte to Binary Representation

## Slide 9: Understanding Raw DLU Logs
3 repeating components in-order:
Header Byte Sequence (HBS)
(31 Bytes)
 Timestamp
Record Byte Sequence (RBS)
(1262-2522 Bytes)
 Record Data
Nullish Byte Sequence (NBS)
(Variable Length)
 Record Delimiter OR
 Corrupt Data

## Slide 10: OMAP’s Base Configuration files
Decoded RBS: A binary stream converted to a
delimited string, correspondent to each parameter
RBS: 01010100 00010100 01111000 10110000…
First_bit_position: 8 , Bit_count: 8
Bit-Set: 00010100
Display-Type: Hexadecimal
String Value: 0x14
Now, We Can Reverse-Engineer OMAP’s Decoding Algorithm

## Slide 11: High-Level Overview - Frontend

## Slide 12: High-Level Overview - Backend

## Slide 13: Design Challenges
The HBS & RBS come After the Nullish Byte Sequence (NBS)
The NBS is Variable in length & value
  Therefore, how do we determine the bit positions of the HBS & RBS?
Impossible to predict the preliminary sequence – How do we find a constant?
  Work backwards; the HBS will tell you in itself
  HBS

## Slide 14: Design Challenges
HBS of non-correlated files & records

## Slide 15: Design Challenges
Is 0xA00101 a ‘secure’ sequence?
  In a Nullish Byte Sequence (NBS) of M bytes (n = 256), what is the probability that 0xA00101 (K = 3) appears at least once?
    If X is the number of times the sequence appears, then
    Upper-bound for
    ATP NBS is usually 1262 bytes long
Therefore, we can use this sequence as our RBS delimiter

## Slide 16: Demonstration
CABS  Invalid

## Slide 17: Demonstration
To determine why CABS is lost, analyze:
· Cabin of driver
· C1 V TF 2 block id
· C2 V TF 2 block id
· Filtered Stop
· CABS_Available
· ATO_Available
· VIO1_FDI_6 – ATO Pushbutton Contact #1 in A1 Car
· VIO1_FDI_7 – ATO Pushbutton Contact #2 in A1 Car
· VIO2_FDI_6 – ATO Pushbutton Contact #1 in A6 Car
· VIO2_FDI_7 – ATO Pushbutton Contact #2 in A6 Car
· VIO1_SafetyInput_3 – ATC Mode Selector set to RM in A1 Car
· VIO1_SafetyInput_4 – ATC Mode Selector set to ATC in A1 Car
· VIO1_SafetyInput_8 – ATC Mode Selector set to MAN in A1 Car
· VIO1_Safety Input_10 – ATC Mode Selector set to OFF in A1 Car
· VIO2_SafetyInput_3 – ATC Mode Selector set to RM in A6 Car
· VIO2_SafetyInput_4 – ATC Mode Selector set to ATC in A6 Car
· VIO2_SafetyInput_8 – ATC Mode Selector set to MAN in A6 Car
· VIO2_Safety Input_10 – ATC Mode Selector set to OFF in A6 Car

## Slide 18: Demonstration Summary
We can come to a summary like this from our analysis

## Slide 19: Current Status
This project attempts a full understanding of Raw DLU Logs & OMAP
More work is needed to further understand NBS & its variability
Frontend runs client-side through HTML file
Backend runs through Drag & Drop of Config.cmd file
Decoding Algorithm has been optimized fully for performance
  ~7.6 seconds for ATO files on Industrial Laptop (18,500,000 Operations)
  ~2.4 seconds for ATP files on Industrial Laptop (6,300,000 Operations)

## Slide 20: Future Enhancements
Bypass the creation of an entire processed .txt file
  Don’t decode every parameter, only decode selected parameters
Expand compatibility for compressed DLU logs

## Slide 21: Questions and Comments?